## Slide 1: E-Portfolio ESP8266
WiFi - Microcontroller

## Slide 2: Contents
About the ESP
Models
Setup / Programming
Communication to Arduino
Examples
Coding

## Slide 3: About
WiFi – module (Full TCP/IP stack)
  Can be used a a web client or server
32-Bit-Microcontroller
Cheap (~3€)
Decent range
IOT (Weather station / LED controlling / …)

## Slide 4: About
SDK is open source
Runs on 3.3V logic!
C++ / Micropython / At-Commands
  AT: Used to configure modems / routers
  However you can also configure it using C++ / Python

## Slide 5: Versions
ESP Version-01
  8 Pins
  Flashing via. USB – UART- Converter
ESP-WROOM-02
  18 Pins
  Existing USB - port

## Slide 6: Versions
Big variety of versions, the principle stays the same
ID | Usage
RX | Serial Input
VCC | Voltage Supply
GPIO 0 | HIGH = Flashing
RESET | LOW = RESET (Pullup to high)
GPIO 2 | HIGH
CH_PD | LOW = Power Down (Chip not running)
GND | Ground
TX | Serial Output

## Slide 7: Setup - Hardware
USB Cable
USB -> UART Converter
  You can also use an Arduino -> Bridge RST to GND
5V to 3.3V Converter
Breadboard for connecting pins / reset button
  Connect like shown in the hardware diagram

## Slide 8: Setup - Hardwarediagram

## Slide 9: Setup - Software
Many IDEs can be used, in my case Arduino IDE
  Download ESP – Core for Arduino IDE
  Select board from board manager
  Upload

## Slide 10: Programming
The ESP8266WiFi.h library includes all the necessary functions such as:
Code | Description
WiFi.begin(ssid,pass) | Connecting to network
WiFi.disconnect() | Disconnecting
WiFi.scanNetworks() | Scanning available networks
WiFiClient client | Creating client for requests
WiFiServer server(port) | Creating server

## Slide 11: Programming – Minimal Example

## Slide 12: Communication to other devices / Arduino
What to do when you need more outputs?
  Connect the ESP to another microcontroller
How to communicate?
  Using UART, the arduino mega e.g. supports three hardware serial conenctions
  Start serial communication with the same baud rate
  Set baud rate low to prevent serial buffer overflow!

## Slide 13: Communication to other devices / Arduino
Filter out commands by checking the beginning of the message for keywords.

## Slide 14: Examples - Webclient
Connects to WiFi network
Creates get-request to api.openwathermap.org
Displays response

## Slide 15: Examples - Webserver
Connects to WiFi network
Creates a response site for a get request /hello

## Slide 16: Coding
Weather station
Gets current weather from an API
Sends JSON to an arduino
Arduino displays it on an LCD

## Slide 17: Sources
https://create.arduino.cc/projecthub/ROBINTHOMAS/esp8266-esp-01-webserver-7248ca?ref=tag&ref_id=esp8266&offset=1
https://forum.arduino.cc/index.php?topic=462829.0
http://www.whatimade.today/esp8266-easiest-way-to-program-so-far/
https://de.wikipedia.org/wiki/AT-Befehlssatz
https://en.wikipedia.org/wiki/ESP8266
https://www.espressif.com/en/products/hardware/esp32/overview
http://stefanfrings.de/esp8266/
Images:
http://stefanfrings.de/esp8266/ESP-01.jpg
https://pradeepsinghblog.files.wordpress.com/2016/04/esp8266-5.png?w=470&h=195